Computer Architecture and Design Practice 2 Report
# 1 Part A
## 1.1 Operation of the design
In this part, I implemented dec_stall, dec_load_use and dec_csr_use signals within the bypass_or_stall module. The dec_stall signal is asserted whenever there is an enable downstream (EXE, MEM, WRB) destination operand that will write to the same register as an enable source register operand at the DEC stage. The dec_load_use signal is asserted if there exists a dependency from the destination of a load instruction at the EXE stage and a source operand at the DEC stage. The dec_csr_use is asserted if there exists a dependency from he destination of a CSR read operation at the EXE stage and a source operand at the DEC stage.
## 1.2 Evaluation of the design
The simulation shows cycle count is 1200, Instruction count is 620 and the average CPI is 1.9. This is because the stall signal will be triggered by any downstream dependencies and reduce the throughput.
The Timing Summary reports that the slack of the critical path is 2.383.
The critical path for part A
The critical path is about branch predictor. It forwards the predict target to the PC at FCH stage if there exists a hit from branch cache.
The execution time of benchmark test is 14.2 seconds.
# 2 Part B
## 1.1 Operation of the design
The dec_rs1_data and dec_rs2_data get the value read from the register file at the beginning. If there is any downstream dependency, the dec_rs1_data and dec_rs2_data will be overwritten by the most recent downstream speculative value. The dec_stall signal is modified to prevent a stall when a speculative downstream value can be used. The first two lines indicate there is no data forwarding and the next two lines indicate that there still exists downstream dependency. I removed the dependency check between DEC stage and WRB stage because the value from the result register of WRB stage is available immediately.
## 1.2 Evaluation of the design
The simulation shows cycle count is 675, Instruction count is 620 and the average CPI is 1.1. The average CPI improves because the modification in this section allows DEC-stage instruction use speculative downstream results. Since there are some stall we cannot remove such as the use of Load result (1-cycle delay), we cannot optimized the CPI to 1.0. In this test, the majority stalls are because of the requirements for the Load result at EXE stage from the DEC stage. There are some pipeline flushes as well, those flushes cost 5 cycles to kill all instructions executing in the pipeline.
The Timing Summary reports that the slack of the critical path is 1.659.
The critical path for part B
The critical path goes through the multiplication logic in EXE, forwards the data to bypass and stall module through mem_result_nxt signal, to the input operand of the divide unit. This critical path slows the execution time and makes the worst time slack smaller to 1.659, where I think the time slack should be larger than part A.
The execution time of benchmark test is 8.5seconds.
# 3 Part C
The critical path mentioned above can be reduced by splitting it into two sequential paths to make time slack bigger. I changed the multiply instruction into 1-cycle delayed operation, which does not allow the value from multiplication to forward from EXE stage to DEC stage. However, the multiplier result can still be forwarded from MEM and WRB and required a stall if the DEC instruction uses the multiplier result from EXE register. This allows a full clock cycle to evaluate the multiplier result.
The simplest modification is letting the dec_load_use be asserted when either load or multiply instruction is evaluated in EXE stage and deleting the path of forwarding the multiplier result from EXE to DEC.